## Slide 1: Exam projects
Nikolay Pavlov

## Slide 2: PIE Factory

## Slide 3: Pie Factory
Pie Factory: pies are made from three components: filling, flavor and topping, each dispensed from a respective hopper with one of these three ingredients.
Robot Lucy
  Adds the three ingredients to empty crusts that move on a conveyor belt.
  Can pause the conveyor belt if a ingredient is depleted.
Robot Joe:
  Fills the hoppers with the respective ingredient.
  Makes sure hoppers are not overfull.
  Makes sure hoppers do not go empty.
Lucy and Joe as separate threads.

## Slide 4: Pie Factory – Process
Belt speed: one pie crust every 50 ms.
One pie takes:
  250 gr filling.
  10 gr flavor.
  100 gr topping.
Every dispensing takes 10 ms.
Hoppers contain 2 kg material max.
Each hopper is filled at speed 100 gr / 10 ms.
Hopper filling start / stop happens immediately.

## Slide 5: Pie Factory - Robots
Robot Lucy:
  1st – adds filling.
  2nd – adds flavor.
  3rd – adds topping.
  Pauses the conveyor belt, if a hopper does not contain enough ingredient for a successful dispense.
  Resumes the conveyor belt once the missing ingredient is available.
Robot Joe:
  Fills one hopper at a time.
  Can fill a hopper only partially.

## Slide 6: Your Task
Implement the factory as a C# program and test it
  Model the hoppers, the robots, and the conveyor belt
  Robots and the belt are serviced by separate threads

## Slide 7: Elevator for Base Area 51

## Slide 8: Elevator for Base Area 51
The base has four floors:
  G – ground floor
  S – secret floor with nuclear weapons
  T1 – secret floor with experimental weapons
  T2 – top-secret floor that stores alien remains
Agents
  Three security levels: Confidential, Secret, Top-secret
  Confidential can access only G floor
  Secret can access G and S
  Top-secret can access G, S, T1 and T2

## Slide 9: Functional Requirements for the Elevator
On each floor there is a button to call the elevator
Inside elevator: four buttons for each floor
  When a button is pressed, all others are disabled until the elevator arrives
When the elevator reaches the floor, the door opens only if the agent inside has the required security credentials.
  If the agent doesn’t have the required credentials, he can press another button to go to another level
The speed of the elevator is 1 floor per 1 sec.

## Slide 10: Your Task
Implement the elevator system as a C# a program and test it by letting agents of different security levels use the elevator repeatedly
  Model the elevator, agents, the elevator door (security check) and the buttons of the elevator.
  Implement the movement of the elevator and button functionality as required
  Implement the security check before opening the door and letting the agent out

## Slide 11: Explanatory Notes
Each agent is serviced by a separate thread
  Moving around is randomly generated
Elevator is serviced by a separate thread
It is enough to allow one agent in the elevator at a time
  Bonus points if you support more; however, in this case door decides how to open based on the agent with lowest security credentials